2

Specification Syntax

This section presents syntactic conventions that are adhered to throughout this specification.

General Syntax

In general, the extension package follows the X11 protocol syntax conventions. Additions to this syntax are as follows:

The syntax ( . . . ) encloses a set of alternative values.

The syntax [ . . . ] encloses a set of structure components.

Within definitions the following prefixes are used:

–	XieReq:	Protocol request/reply	(for example,  XieReqCreatePhotoflo)

–	XieFlo:	Photoflo element	(for example,  XieFloConvolve)

–	XieEvn:	Protocol event	(for example,  XieEvnPhotofloDone)

–	XieErr:	Protocol error	(for example,  XieErrPhotospace)

–	XieTyp:	Protocol type	(for example,  XieTypProcessDomain)

–	XieVal:	Alternative value	(for example, XieValBandByPixel)

Outside of definitions the prefixes are generally not used:

–	Alternative values are italicized and bold	(for example,  BandByPixel)

–	All others are capitalized and bold	(for example,  CreatePhotoflo)

Core X types are displayed in upper-case	(for example, COLORMAP, WINDOW)

Request Syntax

Requests without a Reply:

XieReqRequestName

arg-1: type-1		1st argument for RequestName

. . .

arg-N: type-N	N-th argument for RequestName

Errors:	none or list of errors specific to RequestName (for example,  FloID)

Events:	none or list of events generated by RequestName (for example, PhotofloDone)

Overview	Describes the basic function of the request.

Parameters	Lists the parameters and gives a brief description of each.

Semantics	Interrelationships between input data, parameters, and output results.

Errors	Table of errors that can be generated and their causes,  for example:

Error	Cause

error-1	Circumstances that generate error-1

. . .

error-N	Circumstances that generate error-N

Requests with a Reply:

XieReqRequestName

arg-1: type-1		1st argument for RequestName

. . .

arg-N: type-N	N-th argument for RequestName

result-1: type-1	1st reply result from RequestName

. . .

result-M: type-M	M-th reply result from RequestName

Errors:	none or list of errors specific to RequestName (for example,  Photomap)

Events:	none or list of events generated by RequestName (for example,  EventName)

Overview	Describes the basic function of the request.

Parameters	Lists the parameters and gives a brief description of each.

Reply data	Lists the parameters and gives a brief description of each.

Semantics	Interrelationships between input data, parameters, and output results.

Errors	Table of errors that can be generated and their causes, for example:

Error	Cause

error-1	Circumstances that generate error-1

. . .

error-N	Circumstances that generate error-N

Syntax of Photo Elements

PhotoElements occur within XIE pipelines (see following chapters for clarification).  The syntax of these elements is as follows:

Photo Elements:

XieFloElementName

src-1: src-type-1	1st source for ElementName (if required)

. . .

src-N: src-type-N	N-th source for ElementName (if required)

param-1: param-type-1	1st parameter for ElementName

. . .

param-M: param-type-M	M-th parameter for ElementName

Errors:	none or list of errors specific to ElementName (for example,  FloAlloc)

Events:	none or list of events generated by ElementName (for example,  ExportAvail	able)

Attributes	Table of PhotoElement output attributes, for example:

Attribute	Value

class	DataClass of output data
		SingleBand	achromatic or index
		TripleBand	trichromatic

type	DataType:
		Constrained	quantization levels is levels (integer data)
		Unconstrained	quantization levels is unknown (may be float data)

width	Width  of output data (in pixels per band)

height	Height of output data (in pixels per band)

levels	Depends on type:
		Constrained	number of quantization levels (per band)
		Unconstrained	unknown

Overview	Describes the basic function of the photo element.

Parameters	Lists the parameters and gives a brief description of each.

Semantics	Interrelationships between input data, parameters, and output results.

Errors	Table of errors that can be generated and their causes, for example:

Error	Cause

error-1	Circumstances that generate error-1

. . .

error-N	Circumstances that generate error-N

Syntax of Events

Events generated by Photo Elements:

XieEvnEventName

instance: XieTypExecutable	< Photoflo instance generating EventName >

phototag: XieTypPhototag	< event Phototag (0 for general Photoflo event) >

type: CARD16		< element type (0 for general Photoflo event) >

value-1: type-1	< 1st value returned by EventName >

. . .

value-N: type-N	< N-th value returned by EventName >

Overview	Description of the event.

Values returned	Description of the values returned.

Syntax of Errors

Errors can be associated with core X11 resources or XIE resources.  In the case of XIE specific error conditions, a distinction is made between errors related to a Photoflo and those that are not.

Core X errors

Normal X errors (with XIE major/minor opcodes) are used where appropriate (for example,  Alloc).

XIE non-Photoflo errors:

XieErrName

xie-error: XieErrName		< error code of Name, offset from first-error >

resource-id: XID		< resource to blame, for example, Photomap >

detail			< 21 bytes available for additional error detail >

Overview	Description of the error.

Values returned	Description of the values returned.

XIE Photoflo related errors:

XieErrFloName

flo-error: XieErrName		< error code for Flo, offset from first-error >

flo-id:CARD32		< executable flo-id>

flo-code: XieErrFloName	< specific error type >

name-space: CARD32		< executable name-space>

phototag: CARD16		< erring Phototag (0 for general Photoflo error) >

type: CARD16		< element type (0 for general Photoflo error) >

detail			< 12 bytes available for additional error detail >

Overview	Description of the error.

Values returned	Description of the values returned.

Syntax of Protocol Encodings

Requests

# of Bytes	Value	Description

1	CARD8	XIE major opcode

1	CARD8	XIE minor opcode

2	CARD16	Request length (total bytes divided by 4)

N		Parameters required by the minor opcode

< 4		Pad (if required)

Requests consist of four (4) bytes of header followed by zero (0) or more additional bytes of data.  If additional bytes of data are needed the entire request is padded to a multiple of four (4) bytes.  The common fields (major/minor opcode and length) are not included in XieReq request definitions.  Bytes not used by a specific minor opcode are not guaranteed to be zero.

Replies

# of Bytes	Value	Description

1	1	Reply

1		Available for reply data

2	CARD16	Sequence number of corresponding request

4	CARD32	Reply length (extra data bytes divided by 4)

24		Available for reply data

N		Extra data beyond standard reply packet

< 4		Pad (if required)

Replies consist of thirty-two (32) bytes followed by zero (0) or more extra bytes of data.  If extra bytes of data are needed the entire reply is padded to a multiple of four (4) bytes.  The common fields (Reply, sequence number, and length) are not included in XieReq reply definitions.  Bytes not used by the reply from a specific request are not guaranteed to be zero.

PhotoElements

# of Bytes	Value	Description

2	CARD16	Element type

2	CARD16	Element length (bytes divided by 4)

multiple of 2	XieTyp(Phototag|Tile)	Element's data source(s) (if required)

N		Parameters as required by element type

< 4		Pad (if required)

A photo element consists of four (4) bytes of header followed by zero (0) or more bytes of element input connection definitions and by zero (0) or more bytes or additional data.  The entire element definition is padded to a multiple of four (4) bytes.  The common fields (element type and element length) are not included in XieFlo element definitions.  Bytes not used by a specific element type are not guaranteed to be zero.

Note: PhotoElements are not protocol requests but, rather, subpackets within another protocol request (that is, ExecuteImmediate, CreatePhotoflo, ModifyPhotoflo, or RedefinePhotoflo).

Events

# of Bytes	Value	Description

1	CARD8	XIE event code

1	<varies>	<event-specific>

2	CARD16	Sequence number

4	TIMESTAMP	Time

24	<varies>	<event-specific>

Events consist of thirty-two (32) bytes.  The common fields (event code, sequence number, and time) are not included in XieEvn definitions.  Bytes not used by a specific event code are not guaranteed to be zero.

Errors

# of Bytes	Value	Description

1	0	Error

1	CARD8	XIE error code

2	CARD16	Sequence number

4	<varies>	<error-specific (often a resource-id)>

2	CARD16	Minor opcode

1	CARD8	Major opcode

21	<varies>	<error-specific>

Errors consist of thirty-two (32) bytes.  Bytes not used by the specific error code are not guaranteed to be zero.